Re-engineered drive rod system including, new drive rods, bearing supports and a new coupler.
-Customer should see zero wobble. We should improve the look of the sides of the parts.
-Customer should see zero hysteresis. This should prevent the first couple of layers being excessively squished. This will also give us the ability to add auto leveling to the system.
Re-located Z switch and contact pad.
-This will eliminate Z switch inconsistency. Customers have reported the switch didn't make good contact with the small M3 bolt it used to hit.
Re-designed Y mount parts.
-This will give us a more consistent mounting of the Y axis. The customer should have less initial setup when mounting the Y axis and first starting up.
New fully enclosed/assembled electronics case.
-This will make adding a second extruder significantly easier for the customer
-We will be able to sell a complete electronics box that a customer wouldn't have to do any wiring in.
-In the case a customer has to replace the box, it will be much easier and safer for them to do so.
-It will aid in the manufacturing process because it can be built stand alone before hand.
New External 400W power supply.
-More power to add on accessories
-Nicer looking
-Molded in power cord for a safer assembly
-Still compatible with Nema C13 Power cords