TAZ 6 Palm and Olive(s)2nd production run change list

Palm Feature	Olive(x)
Add grills over exposed fans, especially the front facing one	Change finish on Igus rods
Stabilizing brace on toolhead	Helix lead screws and nuts
Evaluate Extruder mount for potential failure mode	Standard SD, not micro adapter
Possible lighting of bed	Change ‘Thermal Runaway’ indicator on the LCD to read ‘ Thermal Protection Shutdown’ or something similar
Switch to E3D 40W HC	Slightly enlarge all holes in the z-upper
Switch direction of box opening – hard to put in and pull out
Redraw x carriage parts so that they hopefully have less boolean errors.
Create jig for squaring front and back of frame (like y jig)
Add round boss around 12mm rod heatset holes in both x-ends to prevent cracking
Use individual wires in place of 4cond shield cable when shielding/grounding is not required
SD Card slot wider in sheet metal/modify bezel