Date Completed:
Verified by:
Station 1 Assembled by:
Verified:
- The control box meets the workmanship standard for scratches.
- All inserts and studs required by the design are present.
- The PS wires go red, red, red, black, black, black, green, white, black left to right.
- The tie bases have been inspected for placement and orientation.
- The power entry module is oriented with the fuse tray towards the bottom.
- There are fuses present in the fuse tray on the power entry module.
- The rocker switch is oriented with the circle towards the off side.
- The power entry module and rocker switch are connected according to OHAI.
- The control box fan is oriented so that sticker faces the case wall.
- The screws that hold the fan on have washers and are tight.
Station 2 Assembled by:
- The LCD screen is installed as shown in the OHAI.
Station 3 Assembled by:
- The control box cover fasteners are tightened according to the OHAI.
- The SD card can be inserted without interference.
- The Y-Cable mount is zip-tied to the bed harnesses as shown in the OHAI.
- The harnesses are routed as shown in the OHAI with no pinched wires.
- The ground lugs are on the ground post with the star washer and lock nut.
- 2 rubber feet are installed in the intended locations.
- LCD functions normally
- Case fan spins freely
- 24v extrusion fan turns on and off as intended.
- Hot end temperature controls function as intended.