Movement Study

Overview: The movement system on any FFF printer has essentially the same goal, to position a bed and heated nozzle anywhere that the controller and gcode dictate. The purpose of this study is to attempt to understand a handful of the most promising movement systems, all chosen with the condition that the print surface not move in x or y. The systems were evaluated and compared against each-other in terms of relative stiffness, ease of assembly, moving mass, part count and relative cost.

TLDR findings as of 12/13/16

CoreXY: This system has the advantages of stationary motors, balanced movement (IE moving in y does not rack the x axis), high rigidity and ease of scalability. The disadvantages of this system are that the belts need to be fairly long (4x axis length), the system is extremely dependent on the belts being tensioned equally and to a fairly high tension. The system is also incapable of running 2 independently controlled printheads at the same time (parallel printing or BCN sigma style dual extrusion).

SimpleXY: This system is ideal for large printers where moving mass isn’t as much of a concern, as the x and y will be heavier and unbalanced compared to the corexy. It is more modular than the coreXY, has shorter belts and is capable of running 2 independently controlled toolheads at the same time (the corexy is not).

Delta: This system has the benefits of being able to move a light toolhead around very quickly, symmetry between the 3 axes as well as a completely stationary print surface (bed does not move in z). The disadvantages of the delta are that the toolhead is extremely limited in size and weight, and that the printer needs to be over twice as tall as the build height, making scaling difficult.

Cross-gantry style: This system can be extremely rigid, and like the coreXY, is able to remove all motors from the moving axes. It is the most complex system currently used, using an astounding 12 pulleys and belts and 6 smooth rods. Additionally, any bent rods on the outer perimeter will cause defects in x or y. “At UM we concluded that the IM design does not scale much beyond the current size. After that coreXY or H bot makes more sense.” -Daid

H-Bot: The H-Bot design is similar to the coreXY system, but had the advantage of only using 1 belt, it is among the simplest xy gantry systems, with the lowest part count of any in the study. Because it has a single belt, it has the disadvantage of an extremely long belt length (leading to resonance) and the effect that any y movement will put a large moment on the x axis, racking it if there is any play in the axis.

Tripteron: The tripteron is similar to a delta style configuration in that it has 3 identical arms moving the print gantry. It has the advantage of simple kinematics (1mm at x actuator = 1mm at printhead) and that it is slightly more compact in z than a comparably sized delta. It has the disadvantage of loading all 3 arms in bending in order to achieve movement.
Summary Table
Criteria	Config 1: / Core XY	Config 2: / Simple XY	Config 3: / (Delta)	Config 4: / Cross Gantry Style	Config 5: / H-Bot	Config 6: Tripteron
Relative stiffness	4	3	1	5	2
Ease of assembly	3	4	2	1	5
Moving mass	4	1	5	2	3
Part count	1.19	1.03	1.00	1.91	0.91
Relative Cost	0.94	0.99	1.01	1.60	0.78
	18	15	14	10

1 = Worst 5 = best
Configuration 1, Core XY with Z belt Drive

(Description) Pictures file locations

Summary: So far the coreXY has been the most promising of the motion systems, particularly for large build volume applications.
SO far the main failure point seems to be the dynamic pulleys located on the ends of the x-axis. These experience high side loads during printer movement. It would be best if the dynamic pulley mounts were designed to mount the pulleys in double shear at the very least, and this would be a part that would be best machined instead of printed.

Pros:
+ Supported loading x & y with 2 belts reduces backlash
+ correct belt tension improves squareness
+ conducive for tool changing
+ scalable (belt factor)
++ All fixed motors
+ Marlin supports core xy
+ only requires cable chain to toolhead for X and Y (no moving x motor)

Cons:
- Squareness depends on belt tension
- Possible manufacturing complexity since belt tension has to be just right in production
- Longer belts cause greater resonance (each belt length must be 4xaxis+carriage length)
- Lots of pulleys
- Less known in RR community, could be unseen/longterm issues
- crossing belts/ small xy plane moment
- not really possible to do independent x-carriages
- high loads on the x-end pulleys, these NEED to be in double shear

Configuration 2, Simple XY

Pros:
+ X axis can be built and serviced as a subassembly
+ Shorter belts than coreXY (need to be 2x axis+carriage)
+ Simple kinematics (pure x=x, y=y)
+ Design lends itself well to 2 independent toolheads

Cons:
- X carriage cant be in line with belt path
- More moving mass on y axis
- Imbalance in mass between the x and y axes
- Requires either 2 y motors, and additional belt+s pulleys or for the y axis to be heavily cantilevered
- With the x motor on the side of the axis things get pretty crowded, leads to complex/hard to print parts.
- There need to be separate cable chains for the x and y axes

Neither:
* This is probably the most widely used XY gantry both in 3D printing and in the CNC world, there shouldn’t be any surprises here

Configuration 3, (Delta)

Pros:
+ Symmetry in axes
+ Great footprint to BV ratio
+ No need for leadscrews or geared steppers
++ Printed part is completely stationary

Cons:
- Can only support a very light toolhead
- The machine needs to be about twice as tall as the BV
- Manufacturing defects cause hard to calibrate for print defects (bowl shaped xy plane)
- Circular build plate

Neither:

Configuration 4, Cross Gantry Style

Pros:
+ There are a lot of examples of companies that have made this work extremely well (UM and UM clones)
+ In the center of the build volume the toolhead is bracing the x and y rods against each other
+ This design has been widely used in the reprap community

Cons:
- “At UM we concluded that the IM design does not scale much beyond the current size. After that coreXY or H bot makes more sense.” -Daid
- The guide rods in x and y rotate, so any bending in these rods will translate into x or y wobble in the print.

Neither:

Configuration 5, Tripteron

The tripteron is similar to a delta style configuration in that it has 3 identical arms moving the print gantry. It has the advantage of simple kinematics (1mm at x actuator = 1mm at printhead) and that it is slightly more compact in z than a comparably sized delta. It has the disadvantage of loading all 3 arms in bending in order to achieve movement.

Pros:
+ symetry in all axes
+ completely stationary particularly
+BV can be open on 3 sides
+ Does not need to be as tall as a delta for the same BV

Cons:
-Z axis holds weight of toolhead and x and y actuators
-All load is transmitted through moments on the arms, sideloading bearings
- any bending of arms or slop in joints translates into movement hysteresis
- Recently patented

Neither:
* New design with no real use cases to study long term issues

Configuration 5, H-Bot

The H-Bot design is similar to the coreXY system, but had the advantage of only using 1 belt, it is among the simplest xy gantry systems, with the lowest part count of any in the study. Because it has a single belt, it has the disadvantage of an extremely long belt length (leading to resonance) and the effect that any y movement will put a large moment on the x axis, racking it if there is any play in the axis.

Pros:
+ single belt
+ low part count, low cost
+simple assembly

Cons:
-moving y racks x
-extremely long belt → resonance
- Recently patented by ssys

Neither: