Eric

Tool Head / Style	Pro’s	Con’s	Rank #1 / Ease of / Mfg	Rank #2 / Community / Support

Hybrid BDD	+ Balance between material choices and tool head weight / +Minimal hysteresis.	- 2 manufacturers doing; one licensed; possible patent issues / - Flexy tool extenders result in too much hysteresis(Not sure this would be the case.) / - Still; resists movement. Need stiffer system / - Auto Tool head change concept difficult / - Movement of toolhead position in x y or z may rotate shaft when not desired / -May require greater motor torque to get same throughput as direct drive. / -Has minimal testing and information.	3	3
Bowden	+ Small tool head (lightest) / + Perceived to be better / + Smaller extruder spacing; good for a dual / + Easy for long “low interference” wire printing tool / + remote extruder allows stronger drives (geared steppers, dual drive, etc) / +easy maintenance for hob bolt / +Mixing, switching, multi-filament heads possible / + easy to replace individual parts.	- Difficult loading filament / - Hot swap filament sucks / - Unreliable using compressible materials like NinjaFlex / - High Friction filaments get stuck / - Brittle materials problematic / -Tube / -Longer retract distances can increase print time. / -Extruder issues harder to diagnose than direct drive. / -Irregularities in filament have better chance of causing feeding issues	1	2
Direct Drive	+ Material Choices / + Great filament control / + Easy maintenance for hob bolt / + Active community / + Articulated tool head easier / + Easier to be modular / + Highest flow rate for filament driven / + Better hot end control / + Easiest toolhead to troubleshoot if problems arise / +extensive in house testing	- heavier than B/DA / - difficult to make compact size / -Toolhead weight can reduce printing speed.	2	1
Pellet Fed	+ Large Printer/cost reduction for LP / +custom materials	- Huge tool head / - Retraction is not possible, must design alternate method to stop material flow / - limited in-house competencies	???	5
Drive Assist	+ Lighter than DD	- difficult loading filament / - Hot swap filament sucks / - Multiple motors increase POF / - Unreliable using compressible materials like NinjaFlex - Minimal Docs/Less known - High technical complexity	4	4

Criteria	Bowden	Direct Drive

Lighter Toolhead
Multiple head capability
Easy swap heads/Nozzle
Cost
High Temp Capabilities

Bowden
Direct Drive

Hybrid BDD
???

Pellet Fed

Drive Assist
???