Dolores Log:

Market research:

e3D seems to be leader in standalone high performance hotends in RepRap world
DeltaPrintr – New mini hotend with some interesting characteristics
Olsen style hotends – new ultimakers
Microswiss – Interesting break/nozzle interfaces, coatings ect. Specialize in hotend retrofit kits

Research Discussion:
V3 hotend hopes and dreams – hotend-dolores/v3_hotend_wishlist.odt
Initial vendor discussion notes - hotend-dolores/e3d_notes13122016.odt

Initial design goals:

- Inplace swap of exisiting hexagon. Able to use as much of the existing toolhead as possible and have customers easily upgrade from AO hex to v3
- No welded components
- Match and out perform current hotend in both reliability and function.
- Increase manufacture-ability (mostly lathe work. Mill-turn work ok)
- Eliminate need for sealants

Rev 1 notes
- Groove mount heatsink – milled flat with a 30mm flat to accept a 30mm fan – Eliminating ducts
- 2 thick fins to allow for tapped holes to accept the fan and 2 set screws to retain the heat break
- Flats on heat break to positively locate the break against rotation and being pushed out the heatsink (testing needed. Would like to test for spanner-less torqueing of nozzles using the Hot-Torque method
- Heat block very similar to e3d v6 with the addition of a drilled and tapped hole for the addition of a retention plate and sensor wire.
- Nozzle also similar with a more obtuse nozzle cone angle to allow for better wiper contact in the cleaning sequence for less pad wear.

Rev 2 Notes:
- Fin design revised to accept self tapping screws between fins for fan mounting.
- Center of Heat sink changed from 12-14mm to allow more thread engagement on set screws for heat break
- Changed from flats on heat-break to drilled dimples. This will accept high-hold pointed set screws for even better engagement. This also removes less of the thermal contact between the break and the heatsink allowing for better cooling.
- No changes to block/nozzle

Benefits to current design direction:
- No fan ducts. Better cooling,
- Potenial for spanner-less nozzle torque and removeal
- 6 screws (4fan screws and 2 set screws) to change out everything from the heat-break down with a small change to wire harness.
  - This would allow for interchangeable nozzle sizes, quick swap for clogs, and potentially even accessory blocks (MOAR, high heat, abrasive etc) to be swapped in without the removal of entire toolhead.
- Close to drop in for existing toolhead
- Hex nozzle allows for socket type wrenches for easy torque and removal

Cons:
- Current design shown has shorter melt zone. Potentially reduced flow rate (needs to be tested)
- Requires nozzle to torques while hot to prevent leaks (3Nm approx finger tight)
- Heat sink is larger in diameter (35mm) to accommodate flat for fan. May require changes to existing cooling fan ducts to accommodate.