How to: multi-material printing
1/3/2013 - bam

The lulzbot dual extruder positions a second nozzle just in front of the first with z-adjustment for the front extruder. To use it, you'll need to modify your firmware - the modified marlin firmware is available here (http://devel.lulzbot.com/TAZ/Dual_Extruder-TAZ/Dual_Extruder-V0.75/)). You'll also need to set up slic3r and pronterface
Firmware: In the version of marlin for your generation printer (available here), you'll need to make a few changes in the configuration page and the configuration.adv page. Alternately, you can download the pages at http://devel.lulzbot.com/TAZ/Dual_Extruder-TAZ/Dual_Extruder-V0.75/ and paste them into your version of marlin.

In configuration.h, change the number of extruders to 2, and change the movement settings to account for the second extruder – X,Y,Z,E0,E1 instead of the normal X,Y,Z,E.

In Configuration_adv, add the following line under the movement settings section:

“// This defines the number of extruders
#define EXTRUDERS 2”

Slic3r: Download the a dual extruder configuration for slic3r from http://devel.lulzbot.com/TAZ/Dual_Extruder-TAZ/Dual_Extruder-V0.75/, there are versions for using dual .35mm nozzles as well as dual .5mm nozzles. With this loaded, you should have 2 extruders listed under the Printer Settings page. Leave the location of extruder 1 at (0,0), this is the xy position of the front nozzle. Change the offset for the second extruder to -42 for y and 0 for x as a starting point.
You can calibrate the dual extruder by printing a test part, measuring the error and then compensating by changing these values.

Using the file->combine multi-material STL files tool, you can combine 2 stl's into an xml file (if you're using 2 colors for a part