New Filament Testing Steps Check List

MATERIAL: ______________________________________________________________________
MANUFACTURER: ________________________________________________________________
DATE: ____________________________________________________________________________

□ SDS ANALYSIS
□ Is the SDS Fully Completed by the Manufacturer?: __________________________________
□ All Manufacturer Recommended Settings: _________________________________________
□ Personal Health Risks (Toxic gas/dust, etc.): _______________________________________
□ Environmental Risks: _________________________________________________________
□ Glass Transition Temperature: __________________________________________________
□ Thermal Decomposition/Auto Ignition Temperatures: ________________________________
□ Local Regulations: ___________________________________________________________
□ Disposal Options (Recyclable?): ________________________________________________
□ RESEARCH
□ Other Manufacturer Info: ______________________________________________________
□ Internet and Community Research (Reviews, Settings, Material Properties, etc.):
___________________________________________________________________________________
□ PACKAGING
□ Take Notes: _________________________________________________________________
□ CONSISTENCY CHECK
□ Observable Consistency (texture, color, etc.): ______________________________________
□ Cut Sections for Exposure/Moisture Testing Later
□ Take Diameter Readings: ______________________________________________________ ___________________________________________________________________________________
□ Cut Nibblets of filament looking for any inconsistency: ______________________________
□ Bend Testing (Snap? Deform? Consistent?) (150mm-20mm range): _____________________
□ TEMPERATURE TESTS
□ Find Minimum Extrusion Temp: ________________________________________________
□ Take Notes on the Temperatures In Between: _______________________________________
___________________________________________________________________________________
□ Find Maximum Extrusion Temp (do not exceed 290 C): ______________________________
□ Bed Temperature Tests: ________________________________________________________
□ PRINTING TESTS
□ Choose a Base Profile to Work From: ____________________________________________
□ Make Notes on: Ease of Use, Appearance, Print Quality, Strength, Profile Improvements, etc.)
___________________________________________________________________________________
□ EXPOSURE PRINT TESTS
□ Moisture Test
□ Weigh Sample: ________________________________________________________
□ Expose to Humidity Overnight: ___________________________________________
□ Weigh Samples Again: __________________________________________________
□ Use Sample to Print a Test Model: _________________________________________
□ SUBMIT RECOMMENDATION
□ Fill Out Filament Testing Report and Submit
□ CREATE FILAMENT PROFILES
□ Make a New Material in CURA and Test Profile Edits
□ When Profiles are Acceptable Submit them on code.alephobjects.com